## Slide 1: Networking –Part 3
Bob Marshall, MD MPH MISM
11/2015

## Slide 2: Recap/Intro
Reviewed networking types
Reviewed network devices

## Slide 3: Definition
Network security refers to any activities designed to protect your network
Specifically, these activities protect the usability, reliability, integrity, and safety of your network and data
Effective network security targets a variety of threats and stops them from entering or spreading on your network

## Slide 4: Network Threats
Viruses, worms, and Trojan horses
Spyware and adware
Zero-day attacks, also called zero-hour attacks
Hacker attacks
Denial of service attacks
Data interception and theft
Identity theft

## Slide 5: Security Basics
No single solution protects you from a variety of threats
You need multiple layers of security
Network security is accomplished through hardware and software
The software must be constantly updated and managed to protect you from emerging threats

## Slide 6: Security Components
Network security components often include:
  Anti-virus and anti-spyware
  Firewall, to block unauthorized access to your network
  Intrusion prevention systems (IPS), to identify fast-spreading threats, such as zero-day or zero-hour attacks
  Virtual Private Networks (VPNs), to provide secure remote acces

## Slide 7: Authentication & Firewalls
Once authenticated, a firewall enforces access policies such as what services are allowed to be accessed by the network users
Though effective to prevent unauthorized access, this component may fail to check potentially harmful content such as computer worms or Trojans being transmitted over the network.
Anti-virus software or an intrusion prevention system (IPS) help detect and inhibit the action of such malware
An anomaly-based intrusion detection system may also monitor the network like wireshark traffic and may be logged for audit purposes and for later high-level analysis.

## Slide 8: 1, 2 & 3 Factor Authentication
Network security starts with authenticating, commonly with a username and a password
Since this requires just one detail authenticating the user name —i.e., the password— this is sometimes termed one-factor authentication
With two-factor authentication, something the user 'has’ is also used (e.g., a security token or 'dongle', an ATM card, or a mobile phone)
With three-factor authentication, something the user 'is’ also used (e.g., a fingerprint or retinal scan).

## Slide 9: Public Key Infrastructure
A set of hardware, software, people, policies, and procedures needed to create, manage, distribute, use, store, and revoke digital certificates and manage public-key encryption
Purpose of a PKI: facilitate the secure electronic transfer of information for a range of network activities such as e-commerce, internet banking and confidential email
Required for activities where simple passwords are inadequate authentication method and more rigorous proof required to confirm identity of parties involved in the communication and to validate information being transferred

## Slide 10: PKI continued
Binds public keys with respective user identities by means of a certificate authority (CA)
User identity must be unique within each CA domain.
The third-party validation authority (VA) can provide this information on behalf of the CA
Binding established through registration and issuance process
Depending on assurance level of binding, this may be carried out by software at a CA or under human supervision.
The PKI role that assures this binding is called registration authority (RA)
RA responsible for accepting requests for digital certificates and authenticating the person or organization making the request
In Microsoft PKI, a registration authority is usually called a subordinate CA

## Slide 11: PKI Diagram

## Slide 12: PKI consists of
A certificate authority (CA) that both issues and verifies the digital certificates
A registration authority which verifies the identity of users requesting information from the CA
A central directory—i.e., a secure location in which to store and index keys
A certificate management system[clarification needed]
A certificate policy

## Slide 13: Network Security Controls

## Slide 14: Link vs. End-to-End Encryption

## Slide 15: Virtual Private Network
Virtual private network (VPN) technology uses IP-in-IP tunneling to encrypt and encapsulate the IP datagram that has the private IP addresses of the two end hosts with another IP header that has the source and destination IP addresses as the public IP address of the gateway routers for these two private networks.
Each organization is required to have one or more gateway routers with a public IP address in order to facilitate communication over the public Internet.
As the original IP datagram is encrypted, no intermediate forwarding host in the public Internet can look at the contents of the message.

## Slide 16: VPN Diagram
R1 & R2 – Network Routers

## Slide 17: Different Phases of IP-in-IP Tunneling

## Slide 18: Secure Shell (SSH)
Network protocol that allows a user to securely interact with remote machines by establishing a secure channel for data exchange.
SSH replaced TELNET and other insecure remote shell programs that were used in the past to send information in plaintext, including passwords, to remote systems.
SSH encrypts the information sent over the insecure Internet and thus provides both confidentiality and integrity of data.

## Slide 19: Steps to Establish a Secure Shell

## Slide 20: Transport Layer Security (TLS)
successor of the Secure Sockets Layer (SSL) [18]
cryptographic protocol and it provides secure communication of the datagrams of the transport layer
protocols as part of an end-to-end connection across the network. TLS has been used for a wide-variety of
applications like web browsing, electronic mail, voice-over-IP, instant messaging and etc

## Slide 21: TLS Connection Establishment Mechanism

## Slide 22: IP Security
The IP Security Protocol suite (IPSec) is implemented at the IP layer; does not require any change to existing transport layer and application layer protocols
IPSec primarily designed to address fundamental shortcomings of IP layer such as IP address spoofing, wiretapping and session hijacking.
The following two protocols are used to provide packet-level security for both IPv4 and IPv6:
  IP Authentication Header, AH (Next Header protocol ID: 51) provides integrity, authentication and non-repudiation
  IP Encapsulating Security Payload, ESP (Next Header protocol ID: 50) provides confidentiality, along with authentication and integrity protection

## Slide 23: Kerberos
Authentication protocol used by processes/hosts communicating over an insecure network to verify each other’s identity in a secure manner
Based on the idea that a central server provides authenticated tokens called “tickets” to requesting applications
A ticket is an unforgeable, non-replayable, authenticated object
Security of the protocol depends on the assumption that participating machines maintain loosely synchronized time

## Slide 24: Kerberos Protocol Steps

## Slide 25: Kerberos Weaknesses
Requires continuous availability of trusted ticket-granting server for all access control and authentication checks
Password guessing could still work to get the valid secret key for a user. The whole system is still dependent on the user password
Kerberos does not scale well as the number of service servers is increased
Network services cannot be accessed without obtaining Kerberos authentication. All applications run by users in the network need to go through Kerberos authentication

## Slide 26: Firewalls
Device that filters traffic between a “less trustworthy” outside network and a “protected” inside network
Firewall often implemented in software; basically code running on dedicated computer located in the periphery of network to be protected
All traffic exiting and entering network should go through the firewall.
Hence, the firewall often a bottleneck for network performance
Design often makes use of either “default-deny” or “default-allow” approach

## Slide 27: Firewall Types
Packet filtering firewall controls access to packets based on network address, IP address or port numbers (representing specific transport layer protocols).
Stateful firewalls examine each packet with regards to their overall placement in the packet series belonging to a specific connection
Application proxy firewall acts as intermediate gateway attempting to look not only at packet headers but also at the data inside the packets entering or leaving the network to be protected
Personal firewall is an application program running on a specific computer system
  Can also be configured to function as a virus scanner

## Slide 28: Layered Firewall Approach

## Slide 29: Secure Email
The key requirements [6] for secure e-mail are as follows:
  Confidentiality: E-mail contents should not be exposed on the path from the sender to the receiver
  Integrity: The receiver should see in the e-mail, the same content which the sender sent
  Authenticity: Receiver should be able to verify that the e-mail message indeed came from the sender
  Non-repudiation: The sender of the e-mail cannot deny having sent the message

## Slide 30: S/MIME (Secure/ Multi-purpose Internet Mail Extensions)
Secure e-mail standard commonly used in the Internet. Satisfies all four requirements for secure e-mail design
Four components of S/MIME:
  Encrypted version of the original plaintext (e-mail message header and body)
  Encrypted version of random session key used for symmetric encryption of original message header and body
  Encrypted version of the hash of original e-mail message header and body
  Encrypted version of the sender’s public-key certificate

## Slide 31: Network Attacks
Networks are subject to attacks from malicious sources
Attacks can be from two categories to disrupt the network’s normal operation:
  “Passive” when a network intruder intercepts data traveling through the network,
  “Active” in which an intruder initiates commands

## Slide 32: Passive/Active Attacks
Passive
  Network
  Wiretapping
  Port scanner
  Idle scan
Active
  Denial-of-service attack
  DNS spoofing

## Slide 33: Other Attacks
Man in the Middle
ARP poisoning
VLAN_hopping
Smurf attack
Buffer overflow
Heap overflow
Format string attack
SQL injection
Phishing
Cross-site scripting
CSRF
Cyber-attack

## Slide 34: Wiretapping
Process of extracting information as it flows through a wire
The process of wiretapping differs depending on communication medium used
In cables, wiretapping can be done through the use of a packet sniffer or through inductance
Wireless signals are broadcast through open space and are more susceptible for tapping
Optical fibers are more secure than any other transmission media

## Slide 35: TCP Session Hijacking
TCP session hijacking refers to the act of taking over an already established TCP session and injecting packets into the stream that are processed by the receiver as if the packets are coming from the authentic owner of the session
To successfully hijack an existing TCP session, an attacker has to first desynchronize the session and then inject the intended commands
Attacker injects unfamiliar packets into the data stream and creates an ACK storm and can quickly bring down performance of the network

## Slide 36: Man in the Middle Attack
Attacker can read, modify and insert messages between two communicating parties, without either party knowing that the link between them has been compromised
Must be able to observe and intercept messages between the two victims

## Slide 37: DDoS Attack
This involves breaking into hundreds or thousands of machines all over the Internet
Attacker installs malicious software on all compromised machines (called zombies) and controls them to launch coordinated attacks on victim sites
DDoS attacks normally aimed at exhausting the network bandwidth, overwhelming a router’s processing capacity and breaking network connectivity to the victims

## Slide 38: Zero day/Zero hour attacks
A zero-day (also known as zero-hour or 0-day) vulnerability is an undisclosed computer application vulnerability that could be exploited to adversely affect the computer programs, data, additional computers or a network
It is known as a "zero-day" because, once the flaw becomes known, the application author has zero days in which to plan and advise any mitigation against its exploitation (by, for example, advising workarounds or issuing patches)

## Slide 39: Questions